## Slide 1
State Water Plan Update
Joe Gellici and Alex Pellett
Land, Water and Conservation Division
S.C. Department of Natural Resources
Blackwater Summer Festival
Aiken State Park
June 18, 2016

## Slide 2
South Carolina Water Plan
In 2004, DNR published the second edition of the South Carolina Water Plan incorporating lessons learned from the drought of 1998-2002.
One recommendation is for the development of regional water plans for each major river basin in the State.

## Slide 3
South Carolina’s 8 major river basins
Regional water plans will be developed for each of these basins, the same basins used by DHEC for water-quality assessments and for managing interbasin transfers of water.
Notes: Together with DHEC, it was decided that the regional planning areas should coincide with river basins and that we should use the same basin designations that are used by DHEC in their watershed water quality assessments and for IBT permits.

## Slide 4
Development of the surface water models is just the first step in the development of regional and statewide water plans.
Step 1…
Surface water quantity models

## Slide 5
Groundwater models will be used to predict the impacts of groundwater withdrawals on aquifers, streamflows, and on other users of the aquifer.
Step 2…
Groundwater flow models

## Slide 6
Water-demand forecasts will be made for agriculture, energy, industry, and public-supply at 5-10 year intervals over a 50-year planning period.
Step 3…
Water-demand forecasts

## Slide 7
Step 4…
Regional (basinwide) water plans
Using the models and forecasts, and with oversight from State agencies, stakeholders will begin the process of developing regional water plans for each basin.
An analysis to determine if any water deficits will occur
Management strategies to meet the future demands
Water conservation and drought management recommendations

## Slide 8
Step 5…
State water plan
Upon completion of the regional water plans, the State water plan will be updated by DNR.
Assess the overall condition of water resources in the State
Evaluate statewide trends in water use and availability
Offer water-resource policy and program recommendations
Introduce innovative practices

## Slide 9
Piedmont
Coastal Plain
3,800 ft
Piedmont
Coastal
Plain
FALL
LINE

## Slide 10
Project members:
Bruce Campbell (lead) – USGS (Columbia)
Greg Cherry – USGS (Atlanta)
Jason Fine – USGS (Raleigh)
Groundwater Model
Three-year cooperative project with the U.S. Geological Survey.
Purpose: Update the 2010 groundwater flow model of the SC Coastal Plain.
2010 model report
Alex Butler (lead) – SCDNR (Columbia)
Joe Gellici – SCDNR (Columbia)
Andrew Wachob – SCDNR (Columbia)
http://pubs.usgs.gov/pp/1773/
Notes: Pot maps.

## Slide 11
USGS webpage for the project
http://sc.water.usgs.gov/projects/gw_availability2/
Groundwater Model

## Slide 12
Aiken County Groundwater Model
Three-year cooperative project with the U.S. Geological Survey.
Purpose: Develop a detailed groundwater flow model of Aiken County.
Wells and boreholes used to develop hydrogeologic framework
Wells and coreholes
Geology boreholes
Aiken County model extent
Notes: The pink outline shows the modeling area. The green dots show the locations of monitoring and production wells that will be used to create the hydrogeologic framework of the county. The blue dots are boreholes drilled by the S.C. Geological Survey, which will also be used in the construction of the framework.

## Slide 13
Core samples and
drill cuttings
Geophysical logs
Fossil data
Geologic maps
Notes: Information from the wells and boreholes include lithology from core samples and drill cuttings, geophysical logs, information about the age of the layers (obtained from microfossils), and geologic maps.

## Slide 14
Aquifers and confining units are delineated at each well
Notes: Aquifers and confining units are delineated at each well and borehole to produce the hydrogeologic framework, which is the 3-dimensional spatial representation of the groundwater system. The framework is a 3-dimensional map of the subsurface showing the thicknesses, depths, and lateral extents of the aquifers and confining units.

## Slide 15
A fence diagram depicting aquifers and confining units in Aiken County.

## Slide 16
A 3-D hydrogeologic framework generated from the fence diagram using ARC-Hydro software.

## Slide 17
.
Aiken County Groundwater Model
Bruce Campbell (lead) – USGS
Jim Landmeyer – USGS
Alex Butler – SCDNR
Joe Gellici – SCDNR
http://sc.water.usgs.gov/projects/aiken gw/

## Slide 18
The model will be used to:
Determine groundwater availability.
Evaluate the impacts that pumping has on groundwater and surface water resources and on other groundwater users.
Evaluate future withdrawal scenarios to maximize groundwater use and minimize undesirable effects of pumping.

## Slide 19
Examples of scenarios that can be tested with the model
SCENARIO 1
Base Case: A “base case” simulation comprised of pumping existing wells at their reported 2015 withdrawal rates out to year 2050.
SCENARIO 2
Increased Groundwater Withdrawals: The 2015 withdrawal rates will be increased by 0.5 percent per year to 2050. This scenario will also include any planned future wells and their assumed withdrawal rates.
SCENARIO 3
Drought: The effect of a 10-year drought will be simulated for the years 2020-2030 by reducing the annual average recharge rates by 5 to 10 percent.

## Slide 21
Groundwater Monitoring Site
Aiken State Park
Site C-3

## Slide 22
Tertiary sand aquifer (Gordon)
Black Creek aquifer
(aka, Crouch Branch)
Middendorf aquifer
(aka, McQueen Branch)
Bedrock
Confining unit
Sand
Sand and gravel
Clay
Bedrock (schist)
C-3 Hydrostratigraphy

## Slide 23
Tertiary sand aquifer
37 ft

## Slide 24
Confining unit separating the Tertiary sand aquifer from the underlying Black Creek aquifer
58 ft

## Slide 25
Black Creek aquifer
200 ft

## Slide 26
Confining unit separating the Black Creek aquifer from the Middendorf aquifer
277 ft

## Slide 27
Middendorf aquifer
338 ft

## Slide 28
Contact between Coastal Plain and bedrock
504 ft

## Slide 29
Bedrock (metamorphic rock, schist)
539 ft

## Slide 30
ADR
Missing
data
Middendorf aquifer (485-495 ft)

## Slide 31
Black Creek aquifer (178-188 ft)

## Slide 32
BRN-78 Town Williston
Screen 568-700 ft
C-3 Well cluster Aiken St. Pk.
6 wells from 82 ft to 495 ft
AIK-344 Windsor El. Sch.
Screen 338-404 ft
Groundwater Monitoring Site
Groundwater Monitoring Sites

## Slide 35
Major cones of depression in South Carolina
Savannah
Charleston
Andrews
Hemingway
Florence
Marion
100+ foot water-level declines and saltwater intrusion
200+ foot water-level declines in Middendorf aquifer.
200+ foot water-level declines in Middendorf aquifer.
200+ foot water-level declines in Black Creek aquifer.

## Slide 36
WACCAMAW
1979
LOW COUNTRY
1981
TRIDENT
2002
CAPACITY USE AREAS – Areas where groundwater withdrawals are regulated by the State.
PEE DEE
2004
UNREGULATED
UNREGULATED
Groundwater withdrawal permits are required to withdraw and use groundwater equal to or greater than three million gallons in any month in the counties in these areas.

## Slide 37
Thank You
Enjoy the Festival

## Slide 38
Groundwater occurs just about everywhere.
P i e d m o n t
C o a s t a l P l a i n
10–3,000 gallons per minute from wells
1–300 gallons per minute from wells
WADI - Detects conductive features in the subsurface (water-filled fractures) using low-frequency radio waves transmitted by the Navy.
Center-pivot irrigation system.

## Slide 39
Direction of
groundwater
movement
Groundwater and surface water are connected.

## Slide 40
Direction of
groundwater
movement
Potentiometric map of the Middendorf/McQueen Branch aquifer

## Slide 41
Automated water-level data recorder (ADR)

## Slide 43
Updates to the model will include:
Activating the surficial aquifer model layer
Adding recent groundwater-related data (2005-2015)
  Hydrostratigraphic data
  Water-use data
  Aquifer tests
Refining the model grid in some areas
Incorporating a more detailed representation of the Fall Line area
Re-calibration
Applying the model to a series of 6 scenarios